## Slide 1
EXTERNAL Project PRESENTATION

## Slide 2
Implementation of RCA in both Mentor Graphics and QCA & it’s comparative analysis
Presented By:
Devara Harsha (20P31A04J4)
Padarthi Harshitha (20P31A04J5)
Marisetti Sharan Teja (20P31A04L5)
Vasamsetti Dhanupya (20P31A04O1)
Under the Guidance of :
Mr. Anjaiah Talamala, M.Tech,(Ph.D)
Associate Professor
ECE Department

## Slide 3
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
ABSTRACT
QCA technology is a new platform, which is a transistor less and wire-less technology, hence it is one of the best alternatives to CMOS technology for developing low power and high- speed digital circuits at nano-scale level.
A proposed full adder is designed in QCA and with the help of 4 full adders a 4-Bit Ripple Carry Adder is designed in QCA and compared the results with the existing RCA in QCA.
Also, implemented the 4-Bit Ripple Carry Adder in Mentor Graphics and also done the comparison between the two designs.

## Slide 4
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
CONTENTS
INTRODUCTION TO MENTOR GRAPHICS
IMPLEMENTATION OF FULL ADDER AND FOUR BIT RCA USING MENTOR GRAPHICS
SIMULATION RESULTS OF RCA
INTRODUCTION TO QCA
EXSITING MODEL OF FULL ADDER AND FOUR BIT RCA
PROPOSED MODEL OF FULL ADDER AND FOUR BIT RCA
SIMULATION RESULTS OF FOUR BIT RCA
COMPARISON BETWEEN EXISTING AND PROPOSED DESIGN OF 4-BIT RCA IN QCA
COMPARATIVE ANALYSIS
BAR GRAPHS OF PARAMETERS IN EXISTING AND PROPOSED DESIGN
ADVANTAGES
CONCLUSION

## Slide 5
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Introduction To Mentor Graphics
Mentor Graphics was an electronic design automation (EDA) which is used to design complex VLSI architectures
This includes schematic entry tools for traditional designs and HDL (Hardware Description Language) entry tools for digital designs using languages like Verilog, VHDL, and System Verilog.

## Slide 6
Implementation of Full Adder Using Mentor Graphics
Aditya College of Engineering and Technology
Fig: Full Adder Circuit
IV ECE D, BATCH NO. 4
CARRY
A
B
C
XOR 1
AND 1
XOR 2
AND 2
OR 1
SUM
Fig: Truth Table of Full Adder

## Slide 7
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Fig: Full Adder Test Bench
Fig: Full Adder Symbol

## Slide 8
Fig: RCA Circuit
Fig: RCA Symbol
Fig: RCA Test Bench
Implementation of RCA Using Mentor Graphics
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4

## Slide 9
SIMULATION RESULTS OF RCA
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4

## Slide 10
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Introduction To QCA
QCA technology implements complex VLSI architectures with very less power consumption and achieves high speed at nano-scale level compared to CMOS technology.
QCA works mainly on majority gate
A majority gate consists of 5 cells
A cell consist of 4 Quantum dots
  If electron is in Clock-wise then it is Logic 1
  If electron is in Anti clock-wise then it is Logic 0
Polarization = -1
(Binary 0)
Polarization = 1
(Binary 1)
Quantum Dot
Tunnel Junction
Electron
Fig: Polarization in QCA

## Slide 11
Majority Gate :-
A majority gate consists of 5 cells
Where Orange color represents Fixed polarization
Blue color represents Input
Yellow color represents Output
IV ECE D, BATCH NO. 4
Aditya College of Engineering and Technology
M
M(A,B,C)
A
B
C
Electron
Input B
Input A
Output State Y
Fig: Majority Voter Gate

## Slide 12
IV ECE D, BATCH NO. 4
Aditya College of Engineering and Technology
EXISTING MODEL OF FULL ADDER
Fig: Circuit of Existing Full Adder
Sum
A
B
Cin
Cout
Fig: Truth Table of Full Adder
In existing model the Full Adder consists of 47 cell counts.

## Slide 13
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Cout
S3
S2
S0
S1
Y3
Y1
Y2
Y0
X3
X0
X1
X2
Cin
Fig: Circuit of Existing 4-Bit Ripple Carry Adder
EXISTING MODEL OF FOUR BIT RCA
In the Existing model the Four Bit RCA consists of 262 cell counts with the delay of 1.75 and area of 0.34 µ

## Slide 14
PROPOSED MODEL OF FULL ADDER
Aditya College of Engineering and Technology
Fig: Proposed Full Adder Circuit in QCA
IV ECE D, BATCH NO. 4
Fig: Block diagram of Proposed Full Adder
A
B
C
Cout
Sum
The Proposed model of Full Adder consists of 39 cell counts with 0.06 µ

## Slide 15
Fig: Full Adder Results
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
SIMULATION RESULTS OF PROPOSED FULL ADDER

## Slide 16
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Fig: Block Diagram of Proposed 4-Bit RCA in QCA
A3
B3
3-input xor gate
3-input majority gate
S3
COUT
A2
B2
3-input xor gate
3-input majority gate
S2
A1
B1
3-input xor gate
3-input majority gate
S1
A0
B0
3-input xor gate
3-input majority gate
S0
Cin
PROPOSED MODEL OF FOUR BIT RCA BLOCK DIAGRAM

## Slide 17
IV ECE D, BATCH NO. 4
Aditya College of Engineering and Technology
Fig: Truth Table of 4-bit RCA
 | A |  |  |  | B |  |  |  | Sum |  |  |  | Carry
Cin | A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0 | S3 | S2 | S1 | S0 | Cout
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
TRUTH TABLE FOR FOUR BIT RCA

## Slide 18
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Fig: Proposed 4-Bit RCA Circuit in QCA
A3
B3
A2
B2
A1
B1
B0
A0
Cin
S0
S1
S2
S3
Cout
PROPOSED MODEL OF FOUR BIT RCA
The Proposed model of Four Bit RCA using Four Full Adders consists of 208 cell counts, 1.25 delay and 0.30 µ

## Slide 19
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Fig: Output Generation of 4-bit RCA in QCA
SIMULATION RESULTS OF PROPOSED FOUR BIT RCA

## Slide 20
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Fig: Output Generation of 4-bit RCA in QCA

## Slide 21
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
 | EXISTING CIRCUIT | PROPOSED CIRCUIT
AREA | 0.34 µ | 0.30 µ
CELL COUNT | 262 | 208
DELAY | 1.75 | 1.25
 | EXISTING CIRCUIT | PROPOSED CIRCUIT
AREA |  | 
CELL COUNT | 262 | 208
DELAY | 1.75 | 1.25
COMPARISON BETWEEN EXISTING AND PROPOSED DESIGN OF 4-BIT RCA IN QCA

## Slide 22
COMPARATIVE ANALYSIS
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
Parameters | Full Adder in Mentor Graphics | Full Adder in QCA
Area | 9 µ | 0.06 µ
Transistor Count/ QCA Cell Count | 28 | 39
Parameters | Full Adder in Mentor Graphics | Full Adder in QCA
Area |  | 
Transistor Count/ QCA Cell Count | 28 | 39
Parameters | RCA in Mentor Graphics | RCA in QCA
Area | 34 µ | 0.30 µ
Transistor Count/ QCA Cell Count | 112 | 208
Parameters | RCA in Mentor Graphics | RCA in QCA
Area |  | 
Transistor Count/ QCA Cell Count | 112 | 208

## Slide 23
Chart: 
| [1] | [2] | [3] | [4] | [5] | Proposed
Area | 0.68 | 1 | 0.29 | 0.3 | 0.34 | 0.3
Chart: 
| [1] | [2] | [3] | [4] | [5] | Proposed
Cell Count | 494 | 442 | 308 | 295 | 262 | 208
Fig : Cell count comparison between existing and proposed design
Fig : Area comparison between existing and proposed design
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
BAR GRAPHS OF PARAMETERS IN EXISTING AND PROPOSED DESIGN

## Slide 24
Chart: 
| [1] | [2] | [3] | [4] | [5] | Proposed
Delay | 4.25 | 2 | 2 | 1.5 | 1.75 | 1.25
Fig: Delay comparison between existing and proposed methods
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4

## Slide 25
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
ADVANTAGES
Due to small size of quantum dots which are used in QCA, it has very compact arrangements which reduces the overall size and delay of the circuits.
Also QCA circuits have low power consumption with less delay due to having less cell count.

## Slide 26
QCA full adder circuit is proposed which is designed with minimum number of QCA cells. The proposed full adder requires only 39 QCA cells, an area of 0.06 μm2 to implement its function.
The simulation results shows that the proposed 4-bit Ripple Carry Adder (RCA) requires only 208 QCA cells, an area of 0.3 μm2 and delay of about 1.25 clock cycles to implement its function with enhanced performance in terms of latency, area and QCA Cost.
CONCLUSION
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4

## Slide 27
In future, high-speed adders which play an important role in multiplier designs could be designed and its computational performance could be improved further.
The 4-bit ripple carry adder using QCA are used in Arithmetic Logic Units (ALUs) in processors, Digital Signal Processing (DSP) like DFT and FFT.
FUTURE SCOPE
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4

## Slide 28
Aditya College of Engineering and Technology
IV ECE D, BATCH NO. 4
REFERENCES
[1] Y. Adelnia., A. Rezai, A novel adder circuit design in quantum-dot cellular automata technology, Int. J. Theory Phys. (2018), doi: 10.1007/s10773- 018- 3922- 0 .
[2] H. Cho., E.E. Swartzlander, Adder designs and analyses for quantum-dot cellu- lar automata, IEEE Trans. Nanotechnol. 6 (3) (May 2007), doi: 10.1109/TNANO. 2007.894839 .
[3] T.N. Sasamal , A.K. Singh , U. Ghanekar , Efficient design of coplanar ripple carry adder in QCA, IET Circuits Devices Syst. 12 (5) (2018) 594–605 ©The Institution of Engineering and Technology 2018 .
[4] Y.Z. Barughi, S.R. Heikalabad, A three-layer full adder/subtractor structure in quantum-dot cellular automata, Int. J. Theory Phys. (2017), doi: 10.1007/ s10773- 017- 3453- 0 .